## Slide 1
Left Turn Opposing Through Analysis
Leveraging AASHTOWare Safety
Prepared By:
Ron Knezevich, PE RSP2i
GDOT State Safety Engineering Manager

## Slide 2: Takeaways
A new protected left turn query and network screening was created to expedite our network screenings, and permit reviews
GDOT had an older protected left turn phasing policy that needed modernizing
Service units were used to help us create a data driven policy

## Slide 3: Crash Type We are Looking For

## Slide 4: Protected Left Turns
22% of fatal and serious injury crashes at signals are left turn opposing through maneuver in Georgia
Protected left turns reduce 99% of opposing left turn crashes by when converting from permitted or permitted-protected phasing CMF ID: 333
Left turn signalization options
Image source: https://www.nationalacademies.org/read/25905/chapter/6

## Slide 5: Traditional GDOT Analysis
Left turn opposing through crashes each year
Left turn opposing through
crashes each hour

## Slide 6: When Do We Do this Analysis
Network screenings (proactively)
During signal permit revisions (reactive)

## Slide 7: Issues with GDOT Policy
Only considers crash frequency
Definitive language (lack of engineering judgement & open to liability)
No way to do a network screening for these locations
Difficult to quickly identify if the intersection meets policy in a signal permit review

## Slide 8: New GDOT Guidance
Protected Left Turn Evaluation Filter Logic
Captures a broad crash type that may be left turn opposing
Traffic Signal = Yes
Vehicle Maneuver = Turn Left
Manner of Collision = Angle or Head On
Location at Impact is not On Roadway - Driveway Intersection
The number of Vehicles involved in a crash is 2 or more.
Filter Crash data at Intersections

## Slide 9: Analysis Numetric Did with Service Units
Thanks Derek
Area Type = Urban |  | District |  |  |  |  |  | 
Safety Performance Measure | Percentile | 1 | 2 | 3 | 4 | 5 | 6 | 7
Observed Crashes | 75th | 13 | 11 | 10 | 6 | 11 | 11 | 13
Observed Crashes | 95th | 34 | 30.9 | 27 | 19 | 31 | 29 | 36
Crash Rate | 75th | 0.032 | 0.024 | 0.032 | 0.014 | 0.083 | 0.054 | 0.04
Crash Rate | 95th | 0.095 | 0.233 | 0.158 | 0.048 | 0.266 | 0.277 | 0.128
ePDO | 75th | 107.7 | 92.5 | 74.7 | 29.7 | 108.0 | 115.2 | 107.7
ePDO | 95th | 447.6 | 303.5 | 316.4 | 210.1 | 375.7 | 509.3 | 437.3

## Slide 10: Number of intersections by Evaluation Tier

## Slide 11: Filters Used in Analysis

## Slide 12: Scanning Intersections on Crash Query

## Slide 13: Inspecting an Intersection on Crash Query

## Slide 14: Further Inspection on Collision Diagrams for Project Specific Recommendations

## Slide 15: Protected Left Turn Network Screening

## Slide 16: Protected Left Turn Network Screening

## Slide 17: Takeaways
A new Protected left turn query and network screening was created to expedite our network screenings, and permit reviews
GDOT had an older protected left turn phasing policy that needed modernizing
Service units were used to help us create a data driven policy

## Slide 18: Thank you Questions? Ideas?
Ron Knezevich, PE RSP2i
GDOT State Safety Engineering Manager
Rknezevich@dot.ga.gov